## Slide 1
China-Japan Collaborative Site Testing in West China
- A report by Japanese group -
Toshiyuki Sasaki (NAOJ)
on behalf of Site Survey Team
Prof. Yongqiang Yao (NAOC/China),
M. Yoshida(Hiroshima-u), N. Ohshima, Y. Mikami, N. Okada, H. Koyanao,
S. Nagayama, K. Sekiguchi , H. Ando (NAOJ/Japan),
L. Liu (NAOC) and Chinese collaborators
Contents
Background and monitoring instruments
Site monitor showing good conditions in winter at Oma/Tibet
- Clear Sky ratio observed with CloudMon
- image deterioration measured with micro-thermal (CT2) sensors
SiteSurveyWS_201204Beijing_Sasaki.pptx
SiteSurveyWS_201204Beijing_Sasaki.pptx

## Slide 2
China-Japan Collaborative Site Testing in West China
- A report by Japanese group -
Toshiyuki Sasaki (NAOJ)
on behalf of Site Survey Team
Prof. Yongqiang Yao (NAOC/China),
M. Yoshida(Hiroshima-u), N. Ohshima, Y. Mikami, N. Okada, H. Koyanao,
S. Nagayama, K. Sekiguchi , H. Ando (NAOJ/Japan),
L. Liu (NAOC) and Chinese collaborators
Contents
Background and monitoring instruments
Site monitor showing good conditions in winter at Oma/Tibet
Telescope Plan near Ali and possible 4m telescope in future for Asian astronomers
SiteSurveyWS_201204Beijing_Sasaki.pptx
SiteSurveyWS_201204Beijing_Sasaki.pptx

## Slide 3
Collaborative Site Testing in West China
Summary
1) Site Survey and testing has been conducted since 2003, led by Prof. Y. Yao, and two weather-monitoring stations have been settled at Karasu (Xinjiang) and Oma (Tibet).
2) Japanese team has joined the site survey project after the workshop at Lhasa, 2004. We introduced MIR cloud monitor cameras , atmospheric micro-turbulent CT2 sensors, and weather stations at both sites.
At Oma site, cloud monitor camera revealed excellent sky conditions in winter, but not good in summer.
Nominal seeing measured with CT2 was less than 0.1 arcsec up to 36m
height in Nov. 2008. We must conduct seeing measurement through whole
atmosphere w/ DIMM/MASS/(SNODAR) to evaluate seeing condition
at the site soon.
Strong winds have been observed at Oma in winter season, which may affects seeing seriously.
We are settling site survey instruments at possibly best site near Ali in
west Tibet.
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 4
Collaborative Site Testing in West China
Summary
1) Site Survey and testing has been conducted since 2003, led by Prof. Y. Yao, and two weather-monitoring stations have been settled at Karasu (Xinjiang) and Oma (Tibet).
2) Japanese team has joined the site survey project after the workshop at Lhasa, 2004. We introduced MIR cloud monitor cameras , atmospheric micro-turbulent CT2 sensors, and weather stations at both sites.
At Oma site, cloud monitor camera revealed excellent sky conditions in winter, but not good in summer.
Nominal seeing measured with CT2 was less than 0.1 arcsec up to 36m
height in Nov. 2008. We must conduct seeing measurement through whole
atmosphere w/ DIMM/MASS/(SNODAR) to evaluate seeing condition
at the site soon.
Strong winds have been observed at Oma in winter season, which may affects seeing seriously.
We are settling site survey instruments at possibly best site near Ali in
west Tibet.
7) We are discussing to deploy a small telescope w/some observation instruments and negotiating to introduce a possible 4m telescope near Ali.
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 5
A site in west Tibet is in an important location for global astronomical observation network
sites in west China; Karasu, Oma, and Ali
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 6
In Planning phase of ELT, west China is one of candidate sites
Ｇｌｏｂａｌ Ｃｌｏｕｄ Ｄｉｓｔｒｉｂｕｔｉｏｎ
Refer to http://eosweb.larc.nasa.gov/sse/
Meteorology and Solar Energy
Global/Regional Plots
Dr. Sarazin (ESO) showed a global weather map at SPIE at Kona, 2002 .
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 7
Cloud map around west China
Arranged only for night data.
Two blue crosses show Hanle (India)
and Maidanak (Uzbekistan). Red cross
shows candidate site in Tibet.
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 8: Wind Speed at Tibet and Mauna Kea at 200mb
Tibet
Mauna Kea
30m/s
30m/s
From \01SatelliteData\NOAAData\AstronomicalSites\AllSites200mb.xls
Wind speed at 200mb (altitude～12000m) shows correlation with seeing size
Does it mean bad seeing during winter at Tibet? (Vernin 1986 SPIE 628,142)
Winter season
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 9
From \01SatelliteData\NOAAData\AstronomicalSites\AllSites200mb.xls
Local disturbance
may affect local seeing
needs local weather
characterizing
at MKO
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 10
Local disturbance
may affect local seeing
needs local weather
characterizing
From \01SatelliteData\NOAAData\AstronomicalSites\AllSites200mb.xls
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 11
Future telescope plan is considered on base of
Science, Telescope, Instruments and Site.
Site is one of the very important factors for future telescopes.
Site Surevy Project in west China 中国西部選址的協力
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Site Characteristics:
Clear night, less Cloudiness most important !
Seeing
precipitable water vapor
Wind strength
Scale height of ground-layer turbulence
coherence time
wavefront outer scale
dust
Earthquake
Accessibility
Infrastructure at Site:
Access road
Housing / Rest room
Electric Power
Water supply
Lab house
Internet connection
Food, Bed
O2 supply for people at high mountain

## Slide 12
Site monitoring instruments available and/or planned
Instrument Method Measured value Height range
Weather Station* $ Temperature, Humidity, Wind, Pressure Meteorological data at several m
Rain, (Sunshine, IR radiation )
Dust counter* Particle counter Dust particle at several m
Visible whole-sky camera$ visible CCD camera Night sky through atmosphere
IR Cloud monitor* 10μm-band MIR camera Cloudiness through atmosphere
DIMM$ Differential Image Motion Monitor Seeing through atmosphere
MASS $ Multi-Aperture Scintillation Sensor Scintillation 1km to several 10km
SCIDAR $ Scintillation Detection and Ranging Scintillation 1km to several 10km
CT2 sensor * Micro-thermal Turbulence in Surface Layer Turbulence 0 m to several 10 m
SNODAR (planned) Surface layer Non-Doppler Acoustic Radar Scintillation 8m～200m
SODAR (NOT exists) Sound detection and ranging Scintillation 15m～1-2km
$ * Currently available instruments ($China , *Japan )
Cloud Monitor
Weather Station
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
CT2 sensors on 40m tower
(at Ali)
(at Karasu)

## Slide 13
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 14
MASS
(Multi-Aperture Scintillation Sensor)
Figures from V.Kornilov, A.Tokovinin,2004
6 fixed layers model
( 0.5, 1, 2, 4, 8, 16 km)
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 15
・An acoustic pulse into the atmosphere
・Frequency shift of the echo varies according to the wind speed (DOPPLER effect )
・Echo intensity varies according to thermal turbulence and structure.
SODAR
(Sound detection and ranging)
Figures from http://www.remtechinc.com/sodar.htm
52 elements
40 cm x 40 cm x 15 cm in size weight less than 20 kg
SODAR for TMT site survey at MKO(2006)
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 16
DIMM/OAO (Yoshida 2004)
  Meade 20 cm telescope
Two 4cmφ apertures with a separation of 15 cm
  Image-Intensified CCD
  Exposure time = 2 – 6.7 msec
  Data sampling interval = 1/30 sec
automated DIMM at OAO
DIMM/OAO
1 arcsec
Thin cloud
Thin cloud
High Humidity
Dome Closed
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 17
History of Site Survey in West China (Japanese group)
2004 Jul | Lhasa WS on Site Survey and Negotiation starts | 
2006 Mar | MOU between NAOC and NAOJ | 
2007 Mar | Install CloudMon w/ MIR camera at Karasu/Pamir | 
2007 Oct | Install CT2 system at Karasu/Pamir | 
2008 Jul | Relocate CT2 sensors at higher positions Car accident from Kashi to Hotan Visit Hami area. Total eclipse | 
2008 Nov | Install CloudMon, CT2 at Oma/Tibet Install WeatherStation WXT510 at Karasu | 
2009 Oct | Repair CT2 sensor system and replace RAID for data at Oma Extend MOU | 
2010 Dec | Move instruments at Oma to Ali Sasaki got “High altitude sickness” for 3 days in hospital | 
2011 Sep | Install CloudMonitor, Barometer, T-sensors and UPS at Ali | 
2011 Nov | Install WeatherStation WXT510, DustCounter at Ali | 
2012 Apr | Review Site survey project shall extend MOU | 
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 18: Site Monitoring Instruments at Oma (Japanese group)
Cloud Monitor camera
Weather station
and
Barometer
CT2 sensor on 40m tower
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 19
CloudMonitor at Karasu and at Oma
FLIR A40M：
MIR 7.5 to 13 μm
Lens 24° F/1.0 φ36mm
320x240 pixel array, 7.5Hz
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
With mid-infrared camera (7.5 to 13 μm )
to detect cloud distribution with MIR emission of
water vapor

## Slide 20
Cloudiness observed w/ CloudMon at Oma in 2008 and 2009
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 21
Sample Images of CloudMon at Oma on 2008/12/24
All-sky images, every 1 hous, taken w/Cloud Monitor at Oma on 2008-12-24
Ground-based MIR images (Thermal-Eye 2000B Camera, 7-14 μm (320x240 pixel array), 1 frame/ 1 min)
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 22
CloudMonitor Image
2007 March 18 at Karasu
Zenith
Z = 70°
( 20°above horizon )
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 23
Error estimate of cloudiness with Cloud Monitor
Data Analysis
Flat-Fielding, 2) sky subtraction, and 3) masking
Estimated Errors
1) Flat-Fielding image with covered-wth-cap camera with variation of 3.4%.
2) Background intensity variation of 7.7% of flat-fielded images;
a part of variation are due to solar radiation,
but other might be sensitivity variation of the MIR camera.
3) time-dependent variation of sensitivity across the image of 10 - 12%
In total, intensity error might be of 14%.
Due to this large error, we use CloudMonitor images
only for qualitative evaluation of cloudiness so far.
Bias variation
Sensitivity variation
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 24
China-Japan Collaborative Site Testing in West China
Comparison between CloudMon (MIR) image and Visible image
on 2007 March 17 05:35:55UT
Sun
CloudMonitor image
(MIR)
Digital camera
(Visible)
SiteSurveyWS_201204Beijing_Sasaki.pptx
CloudMon detection limit of Cloud w/ 5 % extinction
Using intensity of solar image

## Slide 25
Cloudiness judged w/ CloudMon Images at Oma in 2008 Dec.
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Clear
Fine/fair/partly cloudy
Cloudy/rainy

## Slide 26
Clear sky ratios at Oma, except summer monsoon season, are around 70%, which are comparable to at Mauna Kea, Hawaii, and much bettre than at Okayama, Japan.
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Subaru : statistics during 2000-2010
OAO: summary report during 2008-2009

## Slide 27
Weather Satellite, FY2-D, Image
Chinese Weather Satellite, FY2-D,
is currently working and their data
are available at Chiba-U, Japan
on Web site,
ftp://fy.cr.chiba-u.ac.jp/
( Resolution = 0.04°～ 4km )
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 28
Clouds observed w/Weather Satellite and ground-based CloudMon
Ground-based Monitoring of Clouds in the sky is very useful to evaluate the site,
as weather satellite data is difficult to clarify localized cloud behaviors.
Weather Satellite, FY2-D in IR(10μm)
MIR Cloud Monitor Camera (7-14μm)
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 29
Micro-thermal turbulence detected with CT2 sensors
Related Site testing instruments
・DIMM: Differential Image Motion Monitor
・MASS/SCIDAR: Multi Aperture Scintillation Sensor
・CT2 sensor : Micro-thermal turbulence in surface layer
to measure height variation
・SNODAR: Surface layer Non-Doppler Acoustic Radar to measure Scintillation
・SODAR: Sound detection and ranging to measure Scintillation
Cn2 ∝ P2 T-4 CT2
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Cn2 : refractive index structure coefficient
CT2 : temperature structure coefficient

## Slide 30
CT2 measurements at Karasu and at Oma
Temperature Structure Coefficient
Image deterioration estimated from CT2
A pair of CT2 sensors w/ 25μm Ni wire
Temperature sensor
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 31
CT2 measurements at Karasu and at Oma
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
5 Layers of a CT2 sensor pair
Barometer
Barometer
Karasu
Controller and
Digital Multimeter

## Slide 32
CT2 measurements at Karasu and at Oma
Temperature Structure Coefficient
Seeing estimated from CT2
A pair of CT2 sensors w/ 25μm Ni wire
Temperature sensor
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 33
Micro-thermal turbulence detected with CT2 sensors
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
4.15m
6.25m
10.15m
19.15m
36.65m
at Karasu
Daytime
Nighttime
L1
L2
L3
L4
L5

## Slide 34
Image deterioration estimated with CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
CT2 distribution
at Karasu
Image deterioration derived from CT2 distribution

## Slide 35
Image deterioration estimated with CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
4.15m
6.25m
10.15m
19.15m
36.65m
at Karasu
Daytime
Nighttime
L1
L2
L3
L4
L5

## Slide 36
Layered Image deterioration estimated with CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
4.15m
6.25m
10.15m
19.15m
36.65m
at Karasu
Local Image deterioration between heights of z1 and z0
Daytime
Nighttime
L1
L2
L3
L4
L5

## Slide 37
Scale Height of vertical distribution of CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
derive Zh
at Karasu

## Slide 38
Micro-thermal turbulence detected with CT2 sensors
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
9.65m
14.15m
19.15m
27.65m
36.65m
at Oma
L1
L2
L3
L4
L5

## Slide 39
Image deterioration estimated with CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
CT2 distribution
Image deterioration derived from CT2 distribution
at Oma

## Slide 40
Image deterioration estimated with CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
at Oma
9.65m
14.15m
19.15m
27.65m
36.65m
L5
L1
L2
L3
L4

## Slide 41
Layered Image deterioration estimated with CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
at Oma
9.65m
14.15m
19.15m
27.65m
36.65m
L5
L1
L2
L3
L4

## Slide 42
Scale Height of vertical distribution of CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
derive Zh
at Oma

## Slide 43
Micro-thermal turbulence detected with CT2 sensors
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
3.6m
6m
12m
22m
27m
at OAO (Japan)

## Slide 44
Image deterioration estimated with CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
CT2 distribution
at OAO (Japan)
Image deterioration derived from CT2 distribution

## Slide 45
Image deterioration estimated with CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
at OAO (Japan)
3.6m
6m
12m
22m
27m

## Slide 46
Layered Image deterioration estimated with CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
at OAO (Japan)
3.6m
6m
12m
22m
27m

## Slide 47
Scale Height of vertical distribution of CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
derive Zh
at OAO (Japan)

## Slide 48
Histogram of scale height, Zh , of vertical CT2 distribution
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
at OAO (Japan)
at Karasu
at Oma
Location | GM of Scale Height Zh (meter) | Z of 80%-ile (for Zh>0)
Karasu | 12 m | 16m (@72%)
Oma | 16 m | 30m (@61%)
OAO (Japan) | 13 m | 17m (@70%)
CT2Oma_20091028UT02H_20091111UT10H_Seeing_10min_1.xlsx
CT2Karasu_20071026UT07H_20071115UT01_Seeing_10min_1.xlsx
CT2Okayama_20080205UT01H_20080206UT00H_Seeing_10min_1.xlsx

## Slide 49
Histogram of image deterioration at Zh estimated from CT2
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
at Karasu
at Oma
CT2Oma_20091028UT02H_20091111UT10H_Seeing_10min_1.xlsx
CT2Karasu_20071026UT07H_20071115UT01_Seeing_10min_1.xlsx
Location | Scale Height Zh (meter) | Image Deterio. at Zh (arcsec)
Karasu | 12 m | 0.14
Oma | 16 m | 0.08
OAO(Japan) | 13 m | 0.03
Ave: 0.14”
Ave: 0.08”

## Slide 50
Negative Zh means higher turbulent atmosphere caused by strong wind
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
at Oma
CT2Oma_20091028UT02H_20091111UT10H_Seeing_10min_1.xlsx
Negative Zh
Upper atmosphere should be measured on turbulent motions
with SNODAR (planned).

## Slide 51
Comparison of image deterioration at Zh with seeing by SBIG camera at Oma
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
CT2Oma_20091028UT02H_20091111UT10H_Seeing_10min_1.xlsx
CT2Oma_20091028UT02H_20091111UT10H_Seeing_10min_1.xlsx
SBIG
Camera
CT2

## Slide 52
Comparison of image deterioration at Zh with seeing w/ SBIG camera at Oma
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
CT2Oma_20091028UT02H_20091111UT10H_Seeing_10min_1.xlsx
CT2Oma_20091028UT02H_20091111UT10H_Seeing_10min_1.xlsx

## Slide 53
Weather data at Oma in 2008 and 2009
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Daytime
Nighttime

## Slide 54
Weather data at Oma in 2008 and 2009
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Nighttime
Daytime

## Slide 55
Collaborative Site Testing in West China ( Sasaki et al.)
EACOA in Jeju (Korea), 2010
Weather data at Oma in 2008 and 2009
Wind Speed in winter is typically strong at Oma, which affects local seeing.
For Subaru telescope, operation is limited under Wind Speed of 14 m/sec
and its perfromance is guranteed under 7m/sec.
14m/sec
7 m/sec
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Nighttime
Daytime

## Slide 56
Collaborative Site Testing in West China ( Sasaki et al.)
EACOA in Jeju (Korea), 2010
Weather Direction at Oma in 2008 and 2009
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 57
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Z:\00SiteSurveyData\000_aSiteSurveySummary\
Oma_20091031_CT2_Seeing_WindSpeed_Temp.jpg
Relation among CT2 distribution
and Wind Speed
Sky is clear or fine?
Wind Speed
Temperature
(2009-10-31 at Oma)

## Slide 58
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Z:\00SiteSurveyData\000_aSiteSurveySummary\
Oma_20091031_CT2_Seeing_WindSpeed_Temp.jpg
Relation among CT2 distribution
and Wind Speed
Sky is clear or fine?
Wind Speed
Temperature
(2009-10-31 at Oma)
Zh histogram

## Slide 59
SeismicBigMagCentralAsia_USGS.gif
Earthquake in China
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 60
Candidate Site in Tibet from Satellite Data Site Survey WS at Lhasa, July, 2004
Seismic activity in Tibet
Data from GAME-Tibet project
20060506_SasakiCandidateSiteInTibet.ppt

## Slide 61
Clear sky ratios at Oma, except summer monsoon season, are around 70%, which are comparable to at Mauna Kea, Hawaii, and much bettre than at Okayama, Japan.
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Subaru : statistics during 2000-2010
OAO: summary report during 2008-2009
Location | Scale Height Zh (meter) | Image Deterio. at Zh (arcsec)
Karasu | 12 m | 0.14
Oma | 16 m | 0.08
OAO (Japan) | 13 m | 0.03
CT2 measurements
should evaluate bad effect
of Strong wind at the sites
MIR CloudMonitor

## Slide 62
On-going Collaborative Site Testing at Ali
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Item | Instrument |  | Status
Weather condition | Vaisala:WXT510 |  | Working at Ali
Sky condition | MIR Cloud Mon Visible all-sky camera |  | Working at Ali Working at Ali
Dust | Dust Counter TSI:DustTrak8520 |  | Working at Ali
DIMM | (NAOC) |  | Working (need Manual Operations)
SCIDAR | (NAOC) |  | Working (need Manual Operations)
Surface Layer Turbulence | CT2 sensors on tower |  | Constructed soon this year
Turbulence in upper layer | SNODAR |  | Planning (tomorrow talk)
Housing | w/ electric power |  | Available at Ali
 | O2 supply |  | Comfortable at 5100m !
Road |  |  | need 4WD
Internet | LAN |  | Planned (not yet available stably)
apply site testing instruments with analysis tools to evaluate observational conditions at Ali for years.

## Slide 63
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
The End
謝謝、ありがとう、Thank you！

## Slide 64
Possible Telescope plan at Ali site
After we evaluate and confirm the good condition around Ali,
We’d like to promote to deploy a small telescope w/observation instruments.
- 1m 〜2m Telescope, like TAO 1m telescope made by NISHIMURA’s.
- Optical Imaging/Spectroscopic/Polarimetric Instrument,
like Hiroshima-U’s HOWPol
( HOWPol use two Optical CCDs, which are exported into China easily even now. )
And also we like to introduce a possible 4m telescope near Ali.
A Copy of Kyoto-U 3.8m telescope, under development to install at OAO, Japan.
- Now negotiating to make a copy with Kyoto-U leading people.
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 65
SiteSurveyWS_201204Beijing_Sasaki.pptx
Kyoto 3.8m telescope, possibly installed in west China
http://www.kusastro.kyoto-u.ac.jp/~nagata/Kyoto3m/
- Fan-shaped segmented 18 mirros
light-weighted truss structure
1st light in 2014(?)
China-Japan Collaborative Site Testing in West China
Notes: 車サイズ～1.8m-2.0m 望遠鏡3．8mなので少し大きい表示!

## Slide 66
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 67: Mount of Kyoto 3.8m Telescope
従来の1/5程度の質量
weight～1/5 nomial Telescope
  鏡筒質量8トン（うち構造物：4トン）
54個の主鏡支持点での相対変形<100 μm
relative deformation <100 μm
遺伝的アルゴリズムによる最適化プログラムを開発し、構造の最適化を行った。
Hereditary algorithm
-> Structure optimized (patented)
  高速 駆動 High-speed drive
  低 熱容量 low thermal capacity
  低 熱慣性 low thermal inertia
  低 風抵抗 low wind resistance

## Slide 68: 計測 Mirror measurement
コリメータ
セグメント鏡（曲率半径～10m）
参照面
イメージングレンズ
ハーフミラー
被検光と参照光の光路長が等しい
被検面と参照面を近接して配置
非球面波面の生成に
CGHを使用

## Slide 69
初期解
最適解の一例
許容変形量
0%
200%
Structure optimized with Hereditary algorithm and its FEM analysis

## Slide 70: ２．分割鏡の制御 分割鏡制御の要素
光学センサ：鏡の向きと段差を計測
ギャップセンサ：鏡の段差を計測
支持機構、アクチュエータ：鏡を支持し駆動
プロセッサ：センサ値から指令値を算出
センサ
アクチュエータ
鏡
アクチュエータ
プロセッサ
支持機構
支持機構
図5.28 自己位相測定の方法。
焦点から照射した光の一部をハーフミラーで戻すことで2鏡面での干渉を調べる。
Control of segmented mirrors
Optical sensors
gap sensors
Support and actuators
Control Processors

## Slide 71
Possible Telescope plan at Ali site
Telescope located covering global telescope network
Follow-up observation of GRB to find primordial objects
in the early universe and reveal its characteristics
continuous observations of Blazar, Supernova, nova, X-ray binaries,
cataclysmic variables, variable stars, so on.
- Proper astronomical observations for Asian astronomers
GRB 090423, z=8.2
13.0 billion l.y.
(GRB 090423 : Most distant galaxies ever detected : z= 8.2, 13 b.l.y. )
China-Japan Collaborative Site Testing in West China
SiteSurveyWS_201204Beijing_Sasaki.pptx

## Slide 72
Mauna Kea
4200 m
Ali > 5000 m
〜1m Tel
⇒〜4m Tel
謝謝、ありがとう、Thank you！
Mauna Kea, viewed from Wailoa Park, Hilo
for Asian Astronomers in coming era
Mauna Kea, viewed from Wailoa Park, Hilo
China-Japan Collaborative Site Testing in West China
SiteSurveyWS_201204Beijing_Sasaki.pptx

## Slide 73
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
The End
謝謝、ありがとう、Thank you！

## Slide 74
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 75: Telescope Array at Oma North
1st 8m Tel on the site ～ 2020?
2m Tel for site evaluation ～ 2015?
1st 30m Tel
2nd 30m Tel
30m Tels more … ～ 2040?
launch Interferometry
8m Tels more … ～ 2025?
～ 2030?
～ 2030?
--- Time sequence of Telescope construction
China-Japan Collaborative Site Testing in West China
SiteSurveyWS_201204Beijing_Sasaki.pptx

## Slide 76
Discover New Object
～SN in solar neighberhood!!!
Arrange spectroscopic or
Interferometric observations
Time Lag about 9h
midnight @ MKO
3pm @Oma
Network connection
Coordinated observations
between Subaru and Telescopes at Oma
China-Japan Collaborative Site Testing in West China
SiteSurveyWS_201204Beijing_Sasaki.pptx

## Slide 77: UTs’ random observations and coordinated observation
China-Japan Collaborative Site Testing in West China
SiteSurveyWS_201204Beijing_Sasaki.pptx

## Slide 78: Optical Interferometry 光干渉計 30m Tellescopes 5 ( 10 base lines ) with help of earth rotation, increases base line data → Apply mapping method for image reconstruction Technical developments ・methods for atmospheric dispersion correction (ADC) ・Interferometry with AO → Detailed studies are necessary to promote AOTA.
Merits of Telescope Array
・Each organization possesses own telescope
uses own telescope for their science
・Coordinated operation of Telescope Array for Interferometry
enable high resolution observation, compared to JWST
more faint objects observable than JWST
・Own(80%) vs coordinated(20%) : need MoU
China-Japan Collaborative Site Testing in West China
SiteSurveyWS_201204Beijing_Sasaki.pptx

## Slide 79
One 30m + Several 8m
Two 30m + Several 8m
Several 30m + Several 8m
Visibility lower middle higher
Mag(limit) less faint faint more faint
Cost high higher highest
Feasibility possible maybe possible difficult ??
Which configuration we select ?
China-Japan Collaborative Site Testing in West China
SiteSurveyWS_201204Beijing_Sasaki.pptx

## Slide 80
Cost Estimatation
Site development US$ 10M  MEX budget*
2m telescope US$ 5M  MEX budget*
8m telescope US$200M  fund?
Instruments US$100M  fund?
30m telscope US$600M  fund?
Instruments US$300M  MEX budget*
AOTAI US$500M  fund?
Operation US$100M/year  fund?
*MEX is not so rich, so we find other funds to build AOTA !
China-Japan Collaborative Site Testing in West China
SiteSurveyWS_201204Beijing_Sasaki.pptx

## Slide 81
China-Japan Collaborative Site Testing in West China
SiteSurveyWS_201204Beijing_Sasaki.pptx

## Slide 82
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
The End
謝謝、ありがとう、Thank you！