## Slide 1
China-Japan Collaborative Site Testing in West China
- A report by Japanese group -
Toshiyuki Sasaki (NAOJ)
on behalf of Site Survey Team
Prof. Yongqiang Yao (NAOC/China),
M. Yoshida(Hiroshima-u), N. Ohshima, Y. Mikami, N. Okada, H. Koyanao,
S. Nagayama, K. Sekiguchi , H. Ando (NAOJ/Japan),
L. Liu (NAOC) and Chinese collaborators
Contents
Background and monitoring instruments
Site monitor showing good conditions in winter at Oma/Tibet
- Clear Sky ratio observed with CloudMon
- image deterioration measured with micro-thermal (CT2) sensors
SiteSurveyWS_201204Beijing_Sasaki.pptx
SiteSurveyWS_201204Beijing_Sasaki.pptx

## Slide 2
Collaborative Site Testing in West China
Summary
1) Site Survey and testing has been conducted since 2003, led by Prof. Y. Yao, and two weather-monitoring stations have been settled at Karasu (Xinjiang) and Oma (Tibet).
2) Japanese team has joined the site survey project after the workshop at Lhasa, 2004. We introduced MIR cloud monitor cameras , atmospheric micro-turbulent CT2 sensors, and weather stations at both sites.
At Oma site, cloud monitor camera revealed excellent sky conditions in winter, but not good in summer.
Nominal seeing measured with CT2 was less than 0.1 arcsec up to 36m
height in Nov. 2008. We must conduct seeing measurement through whole
atmosphere w/ DIMM/MASS/(SNODAR) to evaluate seeing condition
at the site soon.
Strong winds have been observed at Oma in winter season, which may affects seeing seriously.
We are settling site survey instruments at possibly best site near Ali in
west Tibet.
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 3
A site in west Tibet is in an important location for global astronomical observation network
sites in west China; Karasu, Oma, and Ali
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 4
In Planning phase of ELT, west China is one of candidate sites
Ｇｌｏｂａｌ Ｃｌｏｕｄ Ｄｉｓｔｒｉｂｕｔｉｏｎ
Refer to http://eosweb.larc.nasa.gov/sse/
Meteorology and Solar Energy
Global/Regional Plots
Dr. Sarazin (ESO) showed a global weather map at SPIE at Kona, 2002 .
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 5
Cloud map around west China
Arranged only for night data.
Two blue crosses show Hanle (India)
and Maidanak (Uzbekistan). Red cross
shows candidate site in Tibet.
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 6: Wind Speed at Tibet and Mauna Kea at 200mb
Tibet
Mauna Kea
30m/s
30m/s
From \01SatelliteData\NOAAData\AstronomicalSites\AllSites200mb.xls
Wind speed at 200mb (altitude～12000m) shows correlation with seeing size
Does it mean bad seeing during winter at Tibet? (Vernin 1986 SPIE 628,142)
Winter season
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 7
From \01SatelliteData\NOAAData\AstronomicalSites\AllSites200mb.xls
Local disturbance
may affect local seeing
needs local weather
characterizing
at MKO
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 8
Site monitoring instruments available and/or planned
Instrument Method Measured value Height range
Weather Station* $ Temperature, Humidity, Wind, Pressure Meteorological data at several m
Rain, (Sunshine, IR radiation )
Dust counter* Particle counter Dust particle at several m
Visible whole-sky camera$ visible CCD camera Night sky through atmosphere
IR Cloud monitor* 10μm-band MIR camera Cloudiness through atmosphere
DIMM$ Differential Image Motion Monitor Seeing through atmosphere
MASS $ Multi-Aperture Scintillation Sensor Scintillation 1km to several 10km
SCIDAR $ Scintillation Detection and Ranging Scintillation 1km to several 10km
CT2 sensor * Micro-thermal Turbulence in Surface Layer Turbulence 0 m to several 10 m
SNODAR (planned) Surface layer Non-Doppler Acoustic Radar Scintillation 8m～200m
SODAR (NOT exists) Sound detection and ranging Scintillation 15m～1-2km
$ * Currently available instruments ($China , *Japan )
Cloud Monitor
Weather Station
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
CT2 sensors on 40m tower
(at Ali)
(at Karasu)

## Slide 9
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 10
Cloudiness observed w/ CloudMon at Oma in 2008 and 2009
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 11
Sample Images of CloudMon at Oma on 2008/12/24
All-sky images, every 1 hous, taken w/Cloud Monitor at Oma on 2008-12-24
Ground-based MIR images (Thermal-Eye 2000B Camera, 7-14 μm (320x240 pixel array), 1 frame/ 1 min)
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 12
CloudMonitor Image
2007 March 18 at Karasu
Zenith
Z = 70°
( 20°above horizon )
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 13
Error estimate of cloudiness with Cloud Monitor
Data Analysis
Flat-Fielding, 2) sky subtraction, and 3) masking
Estimated Errors
1) Flat-Fielding image with covered-wth-cap camera with variation of 3.4%.
2) Background intensity variation of 7.7% of flat-fielded images;
a part of variation are due to solar radiation,
but other might be sensitivity variation of the MIR camera.
3) time-dependent variation of sensitivity across the image of 10 - 12%
In total, intensity error might be of 14%.
Due to this large error, we use CloudMonitor images
only for qualitative evaluation of cloudiness so far.
Bias variation
Sensitivity variation
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 14
China-Japan Collaborative Site Testing in West China
Comparison between CloudMon (MIR) image and Visible image
on 2007 March 17 05:35:55UT
Sun
CloudMonitor image
(MIR)
Digital camera
(Visible)
SiteSurveyWS_201204Beijing_Sasaki.pptx
CloudMon detection limit of Cloud w/ 5 % extinction
Using intensity of solar image

## Slide 15
Cloudiness judged w/ CloudMon Images at Oma in 2008 Dec.
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Clear
Fine/fair/partly cloudy
Cloudy/rainy

## Slide 16
Clear sky ratios at Oma, except summer monsoon season, are around 70%, which are comparable to at Mauna Kea, Hawaii, and much bettre than at Okayama, Japan.
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Subaru : statistics during 2000-2010
OAO: summary report during 2008-2009

## Slide 17
Weather Satellite, FY2-D, Image
Chinese Weather Satellite, FY2-D,
is currently working and their data
are available at Chiba-U, Japan
on Web site,
ftp://fy.cr.chiba-u.ac.jp/
( Resolution = 0.04°～ 4km )
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 18
Clouds observed w/Weather Satellite and ground-based CloudMon
Ground-based Monitoring of Clouds in the sky is very useful to evaluate the site,
as weather satellite data is difficult to clarify localized cloud behaviors.
Weather Satellite, FY2-D in IR(10μm)
MIR Cloud Monitor Camera (7-14μm)
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 19
Micro-thermal turbulence detected with CT2 sensors
Related Site testing instruments
・DIMM: Differential Image Motion Monitor
・MASS/SCIDAR: Multi Aperture Scintillation Sensor
・CT2 sensor : Micro-thermal turbulence in surface layer
to measure height variation
・SNODAR: Surface layer Non-Doppler Acoustic Radar to measure Scintillation
・SODAR: Sound detection and ranging to measure Scintillation
Cn2 ∝ P2 T-4 CT2
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Cn2 : refractive index structure coefficient
CT2 : temperature structure coefficient

## Slide 20
CT2 measurements at Karasu and at Oma
Temperature Structure Coefficient
Image deterioration estimated from CT2
A pair of CT2 sensors w/ 25μm Ni wire
Temperature sensor
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 21
CT2 measurements at Karasu and at Oma
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
5 Layers of a CT2 sensor pair
Barometer
Barometer
Karasu
Controller and
Digital Multimeter

## Slide 22
Micro-thermal turbulence detected with CT2 sensors
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
4.15m
6.25m
10.15m
19.15m
36.65m
at Karasu
Daytime
Nighttime
L1
L2
L3
L4
L5

## Slide 23
Image deterioration estimated with CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
CT2 distribution
at Karasu
Image deterioration derived from CT2 distribution

## Slide 24
Image deterioration estimated with CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
4.15m
6.25m
10.15m
19.15m
36.65m
at Karasu
Daytime
Nighttime
L1
L2
L3
L4
L5

## Slide 25
Layered Image deterioration estimated with CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
4.15m
6.25m
10.15m
19.15m
36.65m
at Karasu
Local Image deterioration between heights of z1 and z0
Daytime
Nighttime
L1
L2
L3
L4
L5

## Slide 26
Scale Height of vertical distribution of CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
derive Zh
at Karasu

## Slide 27
Micro-thermal turbulence detected with CT2 sensors
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
9.65m
14.15m
19.15m
27.65m
36.65m
at Oma
L1
L2
L3
L4
L5

## Slide 28
Image deterioration estimated with CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
CT2 distribution
Image deterioration derived from CT2 distribution
at Oma

## Slide 29
Image deterioration estimated with CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
at Oma
9.65m
14.15m
19.15m
27.65m
36.65m
L5
L1
L2
L3
L4

## Slide 30
Layered Image deterioration estimated with CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
at Oma
9.65m
14.15m
19.15m
27.65m
36.65m
L5
L1
L2
L3
L4

## Slide 31
Scale Height of vertical distribution of CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
derive Zh
at Oma

## Slide 32
Micro-thermal turbulence detected with CT2 sensors
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
3.6m
6m
12m
22m
27m
at OAO (Japan)

## Slide 33
Image deterioration estimated with CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
CT2 distribution
at OAO (Japan)
Image deterioration derived from CT2 distribution

## Slide 34
Image deterioration estimated with CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
at OAO (Japan)
3.6m
6m
12m
22m
27m

## Slide 35
Layered Image deterioration estimated with CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
at OAO (Japan)
3.6m
6m
12m
22m
27m

## Slide 36
Scale Height of vertical distribution of CT2 data
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
derive Zh
at OAO (Japan)

## Slide 37
Histogram of scale height, Zh , of vertical CT2 distribution
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
at OAO (Japan)
at Karasu
at Oma
Location | GM of Scale Height Zh (meter) | Z of 80%-ile (for Zh>0)
Karasu | 12 m | 16m (@72%)
Oma | 16 m | 30m (@61%)
OAO (Japan) | 13 m | 17m (@70%)
CT2Oma_20091028UT02H_20091111UT10H_Seeing_10min_1.xlsx
CT2Karasu_20071026UT07H_20071115UT01_Seeing_10min_1.xlsx
CT2Okayama_20080205UT01H_20080206UT00H_Seeing_10min_1.xlsx

## Slide 38
Histogram of image deterioration at Zh estimated from CT2
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
at Karasu
at Oma
CT2Oma_20091028UT02H_20091111UT10H_Seeing_10min_1.xlsx
CT2Karasu_20071026UT07H_20071115UT01_Seeing_10min_1.xlsx
Location | Scale Height Zh (meter) | Image Deterio. at Zh (arcsec)
Karasu | 12 m | 0.14
Oma | 16 m | 0.08
OAO(Japan) | 13 m | 0.03
Ave: 0.14”
Ave: 0.08”

## Slide 39
Negative Zh means higher turbulent atmosphere caused by strong wind
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
at Oma
CT2Oma_20091028UT02H_20091111UT10H_Seeing_10min_1.xlsx
Negative Zh
Upper atmosphere should be measured on turbulent motions
with SNODAR (planned).

## Slide 40
Comparison of image deterioration at Zh with seeing by SBIG camera at Oma
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
CT2Oma_20091028UT02H_20091111UT10H_Seeing_10min_1.xlsx
CT2Oma_20091028UT02H_20091111UT10H_Seeing_10min_1.xlsx
SBIG
Camera
CT2

## Slide 41
Comparison of image deterioration at Zh with seeing w/ SBIG camera at Oma
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
CT2Oma_20091028UT02H_20091111UT10H_Seeing_10min_1.xlsx
CT2Oma_20091028UT02H_20091111UT10H_Seeing_10min_1.xlsx

## Slide 42
Weather data at Oma in 2008 and 2009
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Daytime
Nighttime

## Slide 43
Weather data at Oma in 2008 and 2009
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Nighttime
Daytime

## Slide 44
Collaborative Site Testing in West China ( Sasaki et al.)
EACOA in Jeju (Korea), 2010
Weather data at Oma in 2008 and 2009
Wind Speed in winter is typically strong at Oma, which affects local seeing.
For Subaru telescope, operation is limited under Wind Speed of 14 m/sec
and its perfromance is guranteed under 7m/sec.
14m/sec
7 m/sec
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Nighttime
Daytime

## Slide 45
Collaborative Site Testing in West China ( Sasaki et al.)
EACOA in Jeju (Korea), 2010
Weather Direction at Oma in 2008 and 2009
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 46
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Z:\00SiteSurveyData\000_aSiteSurveySummary\
Oma_20091031_CT2_Seeing_WindSpeed_Temp.jpg
Relation among CT2 distribution
and Wind Speed
Sky is clear or fine?
Wind Speed
Temperature
(2009-10-31 at Oma)

## Slide 47
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Z:\00SiteSurveyData\000_aSiteSurveySummary\
Oma_20091031_CT2_Seeing_WindSpeed_Temp.jpg
Relation among CT2 distribution
and Wind Speed
Sky is clear or fine?
Wind Speed
Temperature
(2009-10-31 at Oma)
Zh histogram

## Slide 48
SeismicBigMagCentralAsia_USGS.gif
Earthquake in China
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China

## Slide 49
Candidate Site in Tibet from Satellite Data Site Survey WS at Lhasa, July, 2004
Seismic activity in Tibet
Data from GAME-Tibet project
20060506_SasakiCandidateSiteInTibet.ppt

## Slide 50
Clear sky ratios at Oma, except summer monsoon season, are around 70%, which are comparable to at Mauna Kea, Hawaii, and much bettre than at Okayama, Japan.
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Subaru : statistics during 2000-2010
OAO: summary report during 2008-2009
Location | Scale Height Zh (meter) | Image Deterio. at Zh (arcsec)
Karasu | 12 m | 0.14
Oma | 16 m | 0.08
OAO (Japan) | 13 m | 0.03
CT2 measurements
should evaluate bad effect
of Strong wind at the sites
MIR CloudMonitor

## Slide 51
On-going Collaborative Site Testing at Ali
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
Item | Instrument |  | Status
Weather condition | Vaisala:WXT510 |  | Working at Ali
Sky condition | MIR Cloud Mon Visible all-sky camera |  | Working at Ali Working at Ali
Dust | Dust Counter TSI:DustTrak8520 |  | Working at Ali
DIMM | (NAOC) |  | Working (need Manual Operations)
SCIDAR | (NAOC) |  | Working (need Manual Operations)
Surface Layer Turbulence | CT2 sensors on tower |  | Constructed soon this year
Turbulence in upper layer | SNODAR |  | Planning (tomorrow talk)
Housing | w/ electric power |  | Available at Ali
 | O2 supply |  | Comfortable at 5100m !
Road |  |  | need 4WD
Internet | LAN |  | Planned (not yet available stably)
apply site testing instruments with analysis tools to evaluate observational conditions at Ali for years.

## Slide 52
SiteSurveyWS_201204Beijing_Sasaki.pptx
China-Japan Collaborative Site Testing in West China
The End
謝謝、ありがとう、Thank you！